Design Manual
# System Flow Control
The safe cracker is split into a main file, cracker.asm, and helper files which provide functions, macros and interrupt service routines to interact with the AVR board's inputs and outputs. The helper files are described in the 'Modules' section.
The main file, cracker.asm implements the flow of game.
The game is initialised by the reset interrupt service routine. It then enters the main loop which does nothing but wait for interrupts. Interrupts are shown in the diagram with double ended arrows representing the interrupt and return from interrupt.
The interrupt service routine which implements the overall game flow is ovf0handler, the interrupt service routine for the timer 0 overflow interrupt. It executes different sections of code based on the current stage of the game. When the game is over, or if push-button 0 is pushed, it calls restart to restart the game. Otherwise it returns from interrupt to main.
ov1handler and oc1ahandler are interrupt service routines for timer 1 overflow and timer 1 compare match interrupts respectively. These are used to implement LCD fading.
pot_handler is the interrupt service routine for the ADC read complete interrupt, used to implement reading from the potentiometer.
ovf0handler implements the game flow by executing different sections of code based on the stage of the game. The game flow is simply as described by the project specifications.

# Data Structures
Bytes are 8-bit integers. Words are 16-bit (or 2-byte) integers. Characters are (represented as, and can be considered as) bytes. Booleans are stored as bytes.
Key presses and the difficulty level are represented as a character. Letters in this case are represented as capitals (eg the lowest difficulty is 'A').
## cracker.asm
### Registers
timer0_parity is r11, it flips between 1 and 0 on each timer 0 overflow interrupt. It is used to control the fade speed of the LCD.
fade_dir is r12, it stores -1, 0 or 1 to control whether the LCD fades in or out.
lcd_brightness is r13, it stores the current LCD brightness from 0x00 for off to 0xff for full brightness.
cur_code_char is r14, it stores the index of the current character being entered in the enter_code stage.
game_iter is r15, it stores how many rounds have been won/how many secret keys have been found.
tmp is r16, it is used as a miscellaneous temporary variable.
do_display is r22, it stores 1 if the display needs to be refreshed and 0 otherwise.
stage is r23, it stores which stage the stage is at, the stages are defined as constant integer symbols.
tmp_wordl is r24 and tmp_wordh is r25, they are used as a miscellaneous word temporary variable.
### Compiler constant symbols
ticks_per_sec is the approximate number of timer 0 overflows per second.
lcd_fade_time is the number of timer 0 overflows to wait before beginning to fade the LCD.
pot_eps is a small value, below which any potentiometer readings are essentially 0.
start_screen, start_countdown, reset_pot, find_pot, find_code, enter_code, game_complete and timeout are given the values 0 through 7.
### Data segment variables
diff_time is a byte that stores the number of seconds the user has to find the correct potentiometer position in the current difficulty.
diff_level is a character that stores the current difficulty level ('A' to 'D').
timer_cd is word that stores the number of timer 0 overflow interrupts until a second has passed.
timer_cnt is a byte that stores the number of seconds left on the timer.
pot_cd is a word that stores that number of timer 0 overflow interrupts remaining until the potentiometer has been held in the correct position for long enough.
pot_targ is a word that stores the secret target value for the potentiometer.
key_targ is a character that stores the secret target value for the keypad.
key_cd is a word that stores the number of timer 0 overflow interrupts remaining until the secret key has been held for long enough.
key_code is 3 characters that stores the 3 letter code.
strobe_cd is a word that stores the number of timer 0 overflow interrupts remaining until the strobe should be toggled.
lcd_off_cd is a word that stores the number of timer 0 overflow interrupts remaining until the lcd should begin fading.
random_timer is a byte that increments on each timer 0 overflow interrupt and is used to seed the random number generator.
### Program memory constants
The fixed display strings, as specified in the project specifications, are stored as program memory constants. In addition, strings to display each difficulty level, “ (?)” (with ? replaced by the difficulty level as a character) are also stored as program memory constants.
## Modules
The interface to the following helper files is described under 'Modules'. The algorithms used are described in 'Algorithms'. In this section, the data structures used are described.
### keypad-util.asm
pressed_char is a character storing the last pressed character for debouncing purposes.
key_db is a byte storing the remaining debounce duration.
### lcd-fader.asm
LCD fading implicitly stores the LCD brightness in the compare interrupt value for timer 1.
### pot-util.asm
pot is a word that stores the potentiometer reading.
potav is a boolean which stores whether a new potentiometer reading is available.
### rand.asm
rand_cur is a byte that stores the current random value for use in the linear congruential generator.
### speaker-util.asm
speaker_what is a byte that stores 0 or 1 for whether the pin is currently high or low.
speaker_len is a word that stores the remaining speaking duration.
# Algorithms
## cracker.asm
Le todo
## Modules
The interface to the following helper files is described under 'Modules'. The data structures used are described in 'Data Structures'. In this section, the non-trivial algorithms used in the helper files are described.
### keypad-util.asm
read_key is implemented simply by looping over each row of the keypad and then over the columns of that row.
read_key_db implements debouncing by storing the last key pressed, and keeping a counter of how many times a different key or no key needs to be pressed to register new key presses. Once the counter reaches 0, new key presses will be registered.
### lcd-fader.asm
LCD brightness is implemented by turning the LCD on and off, but at small intervals so that the LCD appears to just be dimmer. The greater the proportion of time the LCD is on, the brighter it appears.
Specifically, set_lcd_level sets the proportion of each timer 1 overflow that the LCD will be on. If the level is 5 or lower, the brightness is effectively 0 so the LCD is turned off. Otherwise, each time timer 1 overflows, the LCD is turned on. And each time timer 1 reaches the set level, the LCD is turned off. (Thus a higher LCD brightness level will cause the LCD to be on for a larger proportion of each overflow.)
### lcd-util.asm
print_int is implemented by printing each digit in order: the hundreds digit, then the tens digit then the ones digit, taking care to ignore leading 0s but not non-leading 0s.
### pot-util.asm
pot_handler is the interrupt service routine for the ADC read complete interrupt. It stores potentiometer readings and whether a new reading is available. Then, pot_read simply returns the value of the new reading if one is available (and an invalid value otherwise) and then requests a new reading if needed.
### rand.asm
rand is implemented using a simple linear congruential generator. To create different starting values, the generator is seeded with a timer value when the user begins a new game. Since the timer overflows very often, the seed value is generally random enough.
### speaker-util.asm
Speakers are implemented by simply storing the remaining beep duration. speaker_set_len sets the remaining duration. Then, speaker_speak is run on each timer0 overflow interrupt and switches the pin only if the current beep is not complete.
# Modules
In addition to the main file, a number of helper files define functions, macros and interrupt service routines to interact with the AVR board's inputs and outputs. Only functions, macros and interrupt service routines used in cracker.asm are described.
Macro arguments are referred to as @x (as in avr assembly). a:b represents a pair of registers representing a word, where a is the more significant byte.
### keypad-util.asm
keypad_init (macro): Initialises the keypad.
read_key (function): Returns a key which is currently pressed as a character in r16. If no key is pressed, it returns '?'.
read_key_db (function): Returns a key which is currently pressed as a character in r16 with debouncing. If no key is pressed (or not pressed enough to pass debouncing) it returns '?'.
### lcd-fader.asm
lcd_fade_init (macro): Sets up the LCD for fading.
set_lcd_level (function): Sets the brightness level of the lcd based on r16. When r16 is 0x00 brightness is lowest, when r16 is 0xff brightness is highest.
ovf1handler (interrupt service routine): Interrupt service routine for timer 1 overflow interrupt for LCD fading.
oc1ahandler (interrupt service routine): Interrupt service routine for timer 1 compare match interrupt for LCD fading.
### lcd-util.asm
do_lcd_data (macro): Prints immediate character @0 to the LCD.
lcd_row2 (macro): Moves printing on the LCD to the second row.
lcd_clear (macro): Clears the LCD (and moves printing to the first row).
lcd_init (macro): Initialises the LCD.
rip (function): Prints '*' and infinite loops. Should never be called.
print_int (function): Prints r16 as an integer to the LCD.
### led-util.asm
set_led (macro): Displays the lowest 10 bits of immediate @0 on the LEDs. An LED is turned on if the corresponding bit is set (if the bit is 1). The most significant bit is displayed on the top LED.
### motor-util.asm
motor_init (macro): Initialises the motor.
set_motor_speed (macro): Turns the motor off if immediate @0 is 0, otherwise turns the motor to full speed.
### pb-util.asm
ispb0 (macro): Sets the Z flag to 1 if push-button 0 is pressed. Otherwise sets it to 0.
ispb1 (macro): Sets the Z flag to 1 if push-button 1 is pressed. Otherwise sets it to 0.
is_any_keys (function): Sets the Z flag to 1 if push-button 1 is pressed or any key on the keypad is pressed. Otherwise sets it to 0.
### pot-util.asm
pot_req (function): Initialises the potentiometer. (Used internally to request a reading from the potentiometer.)
pot_read (function): Returns the potentiometer reading in r17:r16. If no reading is available, it returns 0xffff.
pot_handler (interrupt service routine): Interrupt service routine for ADC read complete interrupt for reading the potentiometer.
### print-string.asm
puts (macro): Prints the string at immediate program memory word address @0 to the LCD.
### rand.asm
srand (macro): Seeds the random number generator with r16.
rand (function): Returns a pseudo-random 8-bit integer in r16.
rand_char (function): Returns a (pseudo-)random character on the keypad.
### speaker-util.asm
speaker_init (macro): Initialises the speaker.
speaker_speak (macro): Switches the speaker pin between high and low while the current beep is not completed.
speaker_set_len (macro): Sets the remaining beep duration.
### util.asm
read_word (macro): reads a word from immediate data memory address @2 to registers @0:@1.
write_word (macro): writes a word from registers @0:@1 to immediate data memory address @2.
write_const_word (macro): writes immediate word @1 to immediate data memory address @2.
subi_word (macro): subtracts immediate byte @2 from registers @0:@1. Neither register can be r16.
dec_word (macro): decrement from registers @0:@1. Neither register can be r16.
def_string (macro): places immediate string @0 in program memory with correct padding.