Design Manual
System Flow Control
The safe cracker is split into a main file, 'cracker.asm', and helper files which provide functions, macros and interrupt service routines to interact with the AVR board's inputs and outputs. The helper files are described in the 'Modules' section.
The main file, 'cracker.asm' implements the flow of game.
[flowchart]
Data Structures
Bytes are 8-bit integers.
Words are 16-bit (or 2-byte) integers.
Characters are bytes.
Key presses and the difficulty level are represented as a character. Letters are represented as capitals (eg the lowest difficulty is 'A', not 'a').
Algorithms
## Modules
In addition to the main file, a number of helper files define functions, macros and interrupt service routines to interact with the AVR board's inputs and outputs. Only functions, macros and interrupt service routines used in 'cracker.asm' are described.
Macro arguments are referred to as '@x' (as in avr assembly). 'a:b' represents a pair of registers representing a word, where 'a' is the more significant byte.
### keypad-util.asm
keypad_init (macro): Initialises the keypad.
read_key (function): Returns a key which is currently pressed as a character in r16. If no key is pressed, it returns '?'.
read_key_db (function): Returns a key which is currently pressed as a character in r16 with debouncing. If no key is pressed (or not pressed enough to pass debouncing) it returns '?'.
### lcd-fader.asm
lcd_fade_init (macro): Sets up the LCD for fading.
set_lcd_level (function): Sets the brightness level of the lcd based on r16. When r16 is 0x00 brightness is lowest, when r16 is 0xff brightness is highest.
ovf1handler (interrupt service routine): Handler for timer 1 overflow interrupt for LCD fading.
oc1ahandler (interrupt service routine): Handler for timer 1 compare match interrupt for LCD fading.
### lcd-util.asm
do_lcd_data (macro): Prints immediate character @0 to the LCD.
lcd_row2 (macro): Moves printing on the LCD to the second row.
lcd_clear (macro): Clears the LCD (and moves printing to the first row).
lcd_init (macro): Initialises the LCD.
rip (function): Prints '*' and infinite loops. Should never be called.
print_int (function): Prints r16 as an integer to the LCD.
### led-util.asm
set_led (macro): Displays the lowest 10 bits of immediate @0 on the LEDs. An LED is turned on if the corresponding bit is set (if the bit is 1). The most significant bit is displayed on the top LED.
### motor-util.asm
motor_init (macro): Initialises the motor.
set_motor_speed (macro): Turns the motor off if immediate @0 is 0, otherwise turns the motor to full speed.
### pb-util.asm
ispb0 (macro): Sets the Z flag to 1 if push-button 0 is pressed. Otherwise sets it to 0.
ispb1 (macro): Sets the Z flag to 1 if push-button 1 is pressed. Otherwise sets it to 0.
is_any_keys (function): Sets the Z flag to 1 if push-button 1 is pressed or any key on the keypad is pressed. Otherwise sets it to 0.
### pot-util.asm
pot_req (function): Initialises the potentiometer. (Used internally to request a reading from the potentiometer.)
pot_read (function): Returns the potentiometer reading in r17:r16. If no reading is available, it returns 0xffff.
pot_handler (interrupt service routine): Handler for ADC read complete interrupt for reading the potentiometer.
### print-string.asm
puts (macro): Prints the string at immediate program memory word address @0 to the LCD.
### rand.asm
srand (macro): Seeds the random number generator with r16.
rand (function): Returns a pseudo-random 8-bit integer in r16.
rand_char (function): Returns a (pseudo-)random character on the keypad.
### speaker-util.asm
speaker_init (macro): Initialises the speaker.
speaker_speak (macro): ??????? the magic of sound ?????
speaker_set_len (macro): sets the number of ??? some sound terminology ??? to ???????
### util.asm
read_word (macro): reads a word from immediate data memory address @2 to registers @0:@1.
write_word (macro): writes a word from registers @0:@1 to immediate data memory address @2.
write_const_word (macro): writes immediate word @1 to immediate data memory address @2.
subi_word (macro): subtracts immediate byte @2 from registers @0:@1. Neither register can be r16.
dec_word (macro): decrement from registers @0:@1. Neither register can be r16.
def_string (macro): places immediate string @0 in program memory with correct padding.
…
…
…
blahblah